## Slide 1
Customer Care April Results & Accomplishments
Churn Reduction and Retention Carol Trimmer and Rob Sutton 5/18/2010
  Vonage Holdings Corp. Proprietary & Confidential
  On-Call fraud Procedures
02/25/16

## Slide 2: VoIP Fraud
VoIP fraud can be defined as the unauthorized use of paid communication services charged to someone who isn't expecting it, whether that is the service provider or the customer.
The fraudster looks for a vulnerable (usually publically available) VoIP device, once they have detected one they usually can acquire the SIP credentials for the device.
The Fraudster enters into an agreement with a local exchange telephone carriers in rural areas they then inflate the volume of incoming calls to their network, and make a percentage of the profit off the fees paid.

## Slide 3: Types Of Alerts
Root Alert
These are rated calls that are being charged to the account or Vonage is being charged for the routing i.e International
Domestic Alert
This happens with concurrent calls to any of the 48 states that are not usually rated (Alaska & Hawaii)
Vonage Alert
Carrier Alert which usually has very little info and commonly consists of calls to blacklisted regions or numbers.
Spending Alert
When spending for that account exceeds the set limits of either $300 or $500 (treat as a root alert)

## Slide 4: Investigation Steps
After the Fraud alert comes to the On-Call phone forward that email to yourself in Outlook.
From Outlook “Reply All” (Potential Fraud & CCare On-Call 1) with “Investigating”. Make sure your reply includes your Outlook signature.
Check the Account and see if a ticket was created in Salesforce if not create one. Insure you change case owner to On-Call and place your name in the Tier 2 Rep field.
Copy the notes from the Alert and paste them into the Salesforce Description, be sure to include the type of Fraud Alert i.e.: Root, Domestic, Vonage, or Spending.
Thoroughly investigate the potential Fraud and make your determination whether it’s a False-Positive or Fraud.
From Outlook “Reply All” to the Alert with your investigation notes. (see examples below)
Update your salesforce ticket with your investigation notes in the “Log Call” section change Problem Code to “Fraud Alert” and Problem Code II to reflect False-Positive or Fraud. Make sure case owner is set to On-Call and your name is in the Tier 2 Rep field or you will not be paid.
Close Ticket “Resolved”
Send an email to FraudandAbuseTeam-vb@vonage.com for any actual Frauds at the next day so the total charges can be calculated.

## Slide 5: Begin Your Investigation
You will begin you investigation by looking at the account registration page.
From here you will want to check the IP addresses of any currently registering devices.
You will also want to see if there are any devices registering with duplicate SIP IDs.

## Slide 6: Investigation continued …
Next you will need to bring up the call logs of the extension that set off the Alert.
Search the call logs for the destination number or the terminated number.
Pay close attention to the amount of times the same number was called and the duration of those calls.

## Slide 7: Investigation continued …
Your next step is to bring up the log analyzer for the last call
The Information you will need from here will be the Initiator User Agent which will tell you the device that place the calls, and the Initiator Address which will tell you from where the device was when the calls were placed
Make sure this information is copied and pasted as per the Fraud Template

## Slide 8: Investigation continued …
Use a IP address look up tool (like infosniper.net) to look up the IP address of the Initiator User Agent pay close attention to where these calls were place from.
You will also want to run an MTR to the Initiator User Agent IP address . Look for any signs of High latency, Jitter, or Packet Loss.

## Slide 9: Investigation continued …
You will now want to look at the call logs again. This time look at calls made at least 2 weeks back from the same extension.
You will once again bring up the Log Analyzer from one of these earlier calls.
Compare the information here to the information from the Log Analyzer that set off the Alert.
Check to see if these calls were from a different device, at a different IP address.
If the Device and IP address are the same and there was high latency, jitter, or packet loss this more than likely is a False Positive Alert.
If the Device is different and the location of the IP addresses are far and seem to be suspicious then this could potentially be a Fraud.

## Slide 10: Other ways to investigate.
If after your research you are unclear whether the calls were Fraudulent or not.
You can attempt to call the Account Super User to verify.
You can attempt to place a call to the user on the extension.
If the calls were international check the account to see if there is a history of making these types of calls.
Reach out to your Supervisor or a Fraud SME.